New Logging platform requirements

Currently Kafka and ELK are used as the primary logging service at Swisstopo.
However the platform is used only by a few selected services(mostly Varnish) and letting other services log to it is not a standardized process.

In addition the current platform is still using old components like Elasticsearch 5.2 and is installed as a self-managed solution with instances deployed on AWS.
# Goal, Scope and Distinction of the Project
### Main Goal
The primary goal of the project is to replace the current Platform based on Elasticsearch 5.2.
A new platform should meet and offer all requirements and functionalities the old platform had.
### Additional Goals
- Have a centralized logging platform that is easy to manage
- Have a well defined process to let other services send logs to it
- Have A central User-Interface to analyze the ingested data
### Distinctions
The project considers only Kafka and ELK because the complexity, costs and time consumption of migrating, is most likely much smaller than the migration to a solution based on other products..
Furthermore Elasticsearch know-how is already present at swisstopo and Camp2camp.
# Requirements
## Operations
#	Description	Source	Weight
o1	Management of the platform / Solution should be deployed into AWS	ltmed, ltfrs	must
o2	Minimal effort to update the platform Elasticsearch has rather fast release cycles. It is therefore important that updating the platform is as easy and effortless as possible.	ltfrs	must
o3	Minimal infra complexity / The solution must add as little complexity as possible to the stack.	ltfrs	must
o4	Manual infra scaling / Manual scaling of the underlying infrastructure can be achieved.	lltfrs	must
o4.1	Auto infra scaling / Automatic scaling of the underlying infrastructure can be achieved via metrics such indices sizes and index rate	ltfrs	optional
o5	Costs / Operational costs of the platform must be kept minimal.	ltfrs	must
	User-Interface Security / (Moved to u1)
o6	Support The solution must be agreed by camptocamp, support similar to other resources of the BGDI must be guaranteed.	ltmed, / c2c, ltfrs	must
o7	Monitoring / Monitoring and alerting of the different components shall be as centralized as possible (eg. not having a different dashboard for each service)	ltfrs	Optional

o8	Index migration / Existing indices can be migrated to the new platform. / (Migrating indices from EL 5.x to 7.x can be very complex. We already discussed internally the possibility of a parallel operational phase if needed).	ltjeg	Optional

## Log ingress
#	Description	Source	Weight
i1	Log ingress Security / Log ingress can be encrypted (via TLS, HTTPS, etc.)	ltfrs	must
i2	Complexity and effort for new Services / Complexity and effort to send logs from new services is low and well defined.	Ltmed, ltfrs	Must
i3	Log ingress from «Bundesnetz» / It is possible to ingest logs from «Bundesnetz»	ltch	Must

## User-Interface
#	Description	Source	Weight
u1	Interface security / Users must authenticate themself to access data via the different interfaces (kibana, api, grafana, etc). Applications should be able to authenticate via API keys.	ltfrs	must
u1.2	Fine-grained security / Access to the different Logs (Indices) and Dashboards is configurable	ltmed	must
u2	Access to interfaces is encrypted / Access via HTTPS	ltfrs	must
u3	Dashboards / Current Kibana dashboards can be migrated to the new platform	ltmed	Optional
u4	Emmbedding Dashboards / Dashboards can be emmbedded on websites.	ltoed	Optional

# Evaluation
During the evaluation the following options are considered:

Self-Managed	Install each component by hand on self managed ec2 instances. This is the current setup.
Amazon Elasticsearch Service + MSK	Amazon Elasticsearch Service and Amazon MSK are managed Elasticsearch/Kibana and Apache Kafka services respectively. Since swisstopo is committed to benefit from AWS-managed services this is considered a valid option.
Elastic Cloud	Elastic Cloud is Elasticsearch Inc. own hosted SaaS inside different cloud providers (including AWS).